## Slide 1: Principles of Operating Systems

## Slide 2: Computer System Structures
Computer System Operation
I/O Structure
Storage Structure
Storage Hierarchy
Hardware Protection
General System Architecture

## Slide 3: Computer System Architecture

## Slide 4: Computer System Organization
I/O devices and the CPU execute concurrently.
Each device controller is in charge of a particular device type
  Each device controller has a local buffer. I/O is from the device to local buffer of controller
CPU moves data from/to main memory to/from the local buffers
Device controller interrupts CPU on completion of I/O

## Slide 5: Interrupts
Interrupt transfers control to the interrupt service routine
  Interrupt Service Routine: Segments of code that determine action to be taken for each type of interrupt.
  Interrupt vector contains the address of service routines.
OS preserves the state of the CPU
  stores registers and the program counter (address of interrupted instruction).
Trap
  software generated interrupt caused either by an error or a user request.

## Slide 6: Interrupt Handling
Types of interrupt
  Polling
  Vectored interrupt system
Incoming interrupts are disabled while another interrupt is being processed to prevent a lost interrupt.

## Slide 7: I/O Structure
Synchronous I/O
    wait instruction idles CPU until next interrupt
    no simultaneous I/O processing, at most one outstanding I/O request at a time.
Asynchronous I/O
  After I/O is initiated, control returns to user program without waiting for I/O completion.
    System call
    Device Status table - holds type, address and state for each device
    OS indexes into I/O device table to determine device status and modify table entry to include interrupt.

## Slide 8: Direct Memory Access (DMA)
Used for high speed I/O devices able to transmit information at close to memory speeds.
Device controller transfers blocks of data from buffer storage directly to main memory without CPU intervention.
Only one interrupt is generated per block, rather than one per byte (or word).
Memory
CPU
I/O devices
I/O instructions

## Slide 9: Storage Structure
Main memory - only large storage media that the CPU can access directly.
Secondary storage - extension of main memory that has large nonvolatile storage capacity.
  Magnetic disks - rigid metal or glass platters covered with magnetic recording material.
    Disk surface is logically divided into tracks, subdivided into sectors.
    Disk controller determines logical interaction between device and computer.

## Slide 10: Storage Hierarchy
Storage systems are organized in a hierarchy based on
  Speed
  Cost
  Volatility
Caching - process of copying information into faster storage system; main memory can be viewed as fast cache for secondary storage.

## Slide 11: Storage Device Hierarchy

## Slide 12: Hardware Protection
Dual Mode Operation
I/O Protection
Memory Protection
CPU Protection

## Slide 13: Dual-mode operation
Sharing system resources requires operating system to ensure that an incorrect program cannot cause other programs to execute incorrectly.
Provide hardware support to differentiate between at least two modes of operation:
  1. User mode -- execution done on behalf of a user.
  2. Monitor mode (supervisor/kernel/system mode) -- execution done on behalf of operating system.

## Slide 14: Dual-mode operation(cont.)
Mode bit added to computer hardware to indicate the current mode: monitor(0) or user(1).
When an interrupt or fault occurs, hardware switches to monitor mode.
Privileged instructions only in monitor mode.
User
Monitor
Set
user
mode
Interrupt/
fault

## Slide 15: I/O Protection
All I/O instructions are privileged instructions.
Must ensure that a user program could never gain control of the computer in monitor mode, for e.g. a user program that as part of its execution, stores a new address in the interrupt vector.

## Slide 16: Memory Protection
Must provide memory protection at least for the interrupt vector and the interrupt service routines.
To provide memory protection, add two registers that determine the range of legal addresses a program may address.
  Base Register - holds smallest legal physical memory address.
  Limit register - contains the size of the range.
Memory outside the defined range is protected.
0
256000
3000040
420940
880000
1024000
300040
120900
Base register
Limit register
monitor
Job1
Job 2
Job 4
Job 3
0

## Slide 17: Hardware Address Protection

## Slide 18: Protection Hardware (cont.)
When executing in monitor mode, the OS has unrestricted access to both monitor and users’ memory.
The load instructions for the base and limit registers are privileged instructions.

## Slide 19: CPU Protection
Timer - interrupts computer after specified period to ensure that OS maintains control.
  Timer is decremented every clock tick.
  When timer reaches a value of 0, an interrupt occurs.
Timer is commonly used to implement time sharing.
Timer is also used to compute the current time.
Load timer is a privileged instruction.

## Slide 20: General System Architecture
Given the I/O instructions are privileged, how do users perform I/O?
Via system calls - the method used by a process to request action by the operating system.

## Slide 21: Operating System Structures
Operating System Components
  Process Management, Memory Management, Secondary Storage Management, I/O System Management, File Management, Protection System, Networking, Command-Interpreter.
Operating System Services, System calls, System Programs
Virtual Machine Structure and Organization
A Structural Approach to Operating Systems
OS Design and Implementation

## Slide 22: Operating System Services
Services that provide user-interfaces to OS
    Program execution - load program into memory and run it
    I/O Operations - since users cannot execute I/O operations directly
    File System Manipulation - read, write, create, delete files
    Communications - interprocess and intersystem
    Error Detection - in hardware, I/O devices, user programs
Services for providing efficient system operation
    Resource Allocation - for simultaneously executing jobs
    Accounting - for account billing and usage statistics
    Protection - ensure access to system resources is controlled

## Slide 23: System Calls
Interface between running program and the OS.
  Assembly language instructions (macros and subroutines)
  Some higher level languages allow system calls to be made directly (e.g. C)
Passing parameters between a running program and OS via registers, memory tables or stack.
Unix has about 32 system calls
  read(), write(), open(), close(), fork(), exec(), ioctl(),…..

## Slide 24: System Programs
Convenient environment for program development and execution. User view of OS is defined by system programs, not system calls.
    Command Interpreter (sh, csh, ksh) - parses/executes other system programs
    File manipulation - copy (cp), print (lpr), compare(cmp, diff)
    File modification - editing (ed, vi, emacs)
    Application programs - send mail (mail), read news (rn)
    Programming language support (cc)
    Status information, communication
    etc….

## Slide 25: Command Interpreter System
Commands that are given to the operating system via command statements that execute
  Process creation and deletion, I/O handling, Secondary Storage Management, Main Memory Management, File System Access, Protection, Networking.
Obtains the next command and executes it.
Programs that read and interpret control statements also called -
  Control card interpreter, command-line interpreter, shell (in UNIX)

## Slide 26: Process Management (Chapters 4-7)
Process - fundamental concept in OS
  Process is a program in execution.
  Process needs resources - CPU time, memory, files/data and I/O devices.
OS is responsible for the following process management activities.
  Process creation and deletion
  Process suspension and resumption
  Process synchronization and interprocess communication
  Process interactions - deadlock detection, avoidance and correction

## Slide 27: Memory Management (Chapters 8-9)
Main Memory is an array of addressable words or bytes that is quickly accessible.
Main Memory is volatile.
OS is responsible for:
    Allocate and deallocate memory to processes.
    Managing multiple processes within memory - keep track of which parts of memory are used by which processes. Manage the sharing of memory between processes.
    Determining which processes to load when memory becomes available.

## Slide 28: Secondary Storage and I/O Management (Chapter 10)
Since primary storage is expensive and volatile, secondary storage is required for backup.
Disk is the primary form of secondary storage.
  OS performs storage allocation, free-space management and disk scheduling.
I/O system in the OS consists of
  Buffer caching and management
  Device driver interface that abstracts device details
  Drivers for specific hardware devices

## Slide 29: File System Management (Chapters 11-12)
File is a collection of related information defined by creator - represents programs and data.
OS is responsible for
  File creation and deletion
  Directory creation and deletion
  Supporting primitives for file/directory manipulation.
  Mapping files to disks (secondary storage).
  Backup files on archival media (tapes).

## Slide 30: Protection and Security (Chapter 14)
Protection mechanisms control access of programs and processes to user and system resources.
  Protect user from himself, user from other users, system from users.
Protection mechanisms must:
  Distinguish between authorized and unauthorized use.
  Specify access controls to be imposed on use.
  Provide mechanisms for enforcement of access control.
  Security mechanisms provide trust in system and privacy
    authentication, certification, encryption etc.

## Slide 31: Networking (Distributed Systems)
Distributed System is a collection of processors that do not share memory or a clock.
Processors are connected via a communication network.
Advantages:
  Allows users and system to exchange information
  provide computational speedup
  increased reliability and availability of information

## Slide 32: System Design and Implementation
Establish design goals
  User Goals
  System Goals
Software Engineering -
  Separate mechanism from policy. Policies determine what needs to be done, mechanisms determine how they are done.
Choose a high-level implementation language
  faster implementation, more compact, easier to debug

## Slide 33: System Generation
OS written for a class of machines, must be configured for each specific site.
  SYSGEN program obtains info about specific hardware configuration and creates version of OS for hardware
Booting
Bootstrap program - loader program loads kernel, kernel loads rest of OS.
  Bootstrap program stored in ROM

## Slide 34: OS Structure - Simple Approach
MS-DOS - provides a lot of functionality in little space.
  Not divided into modules, Interfaces and levels of functionality are not well separated
UNIX - limited structuring, has 2 separable parts
  Systems programs
  Kernel
    everything below system call interface and above physical hardware.
    Filesystem, CPU scheduling, memory management

## Slide 35: UNIX System Structure

## Slide 36: Layered OS Structure
OS divided into number of layers - bottom layer is hardware, highest layer is the user interface.
Each layer uses functions and services of only lower-level layers.
THE Operating System Kernel has successive layers of abstraction.

## Slide 37: Virtual Machines
Logically treats hardware and OS kernel as hardware
Provides interface identical to underlying bare hardware.
Creates illusion of multiple processes - each with its own processor and virtual memory
hardware
Virtual machine
kernel
kernel
kernel
processes
processes
processes

## Slide 38: Summary of OS Structures
Operating System Concepts
Operating System Services, System Programs and System calls
Operating System Design and Implementation
Structuring Operating Systems