## Slide 1: Computer Organization Lecture 23 DMA, Exception and interrupt
Subhasis Banerjee
IIIT-D

## Slide 2: Direct Memory Access (DMA)
Three primary data transfer mechanism:
Polling → processor waits for data in a loop
Interrupt driven → An interrupt signal facilitates data transfer
DMA → Direct Memory Access
DMA is faster: processor is not included in the process
One or two bus read/write cycles are required by dedicated hardware
Dedicated hardware support (DMA controller)

## Slide 3: DMA Operation
DMA controller is usually a peripheral device to CPU
DMA controller has right to access memory directly
Can transfer data from one memory location to another
I/O to memory and vice versa
Many DMA channels to facilitate multiple transfer simultaneously (many I/O can be active simultaneously)
Operation:
Devices that are willing / expecting to transfer / receive data send signal to DMA

## Slide 4: DMA

## Slide 5: Advantages and Disadvantages
Advantage:
  CPU is offloaded, data transfer happens without CPU involvement
  CPU is either assigned some other tasks or sent to low power state
Disadvantage:
  Data modified – need to keep the coherence status. More synchronization signals

## Slide 6: Systems with DMA

## Slide 7: Example of DMA
Loading program from disk to memory
  One option: CPU loads first byte copy it to memory (move or load/store operation)
  Other one: DMA: does not include CPU into the loop. Initially an interrupt signal is sent to notify the DMA controller to initiate DMA operation. Source address, Destination address and bytes to transfer is written into control registers. Once the operation is done (memory bus is used as the communication channel) DMA controller sends signals to CPU

## Slide 8: Operation in Detail
Transfer data from I/O -> memory
  DMA controller sends a Bus Request to the CPU (BR to 1)
  When it is ready to grant this request, the CPU sets it’s Bus grant signal, BG to 1
CPU sends it address, data and control line to tri-state, this allows DMA controller to control system buses
CPU continues to tri-state outputs as long as BR is asserted.
DMA Address Register contains the memory address to be used in the data transfer. The CPU treats this signal as one or more output ports.

## Slide 9: Contd..
The DMA Word Count Register contains the # of bytes to be transferred.
This is also treated as an O/P port (with a diff. Address) by the CPU.
The DMA Control Register accepts commands from the CPU

## Slide 10: Exception and Interrupt
Exception: unexpected change in control
Interrupt: caused by external signal